Name:

Geology 340: Images of the Earth

Lab 8 – 3D Visualization in ArcGIS

In this lab we will explore some of the 3D visualization techniques provided in ArcScene.

Part 1:  Guilford Campus

- Download the Lab 8 data from the course web page

- Open ArcScene

- Add the items from the Guilford folder to your ArcScene – this should be:

  - Guiltin – the TIN file with elevations

  - 2-foot topographic lines

  - Lake

  - Rivers

  - Buildings

  - Paved Areas

  - Roads

- Set the base height (under properties) for all of the data sets to the “Guiltin” data set

- Set the buildings to extrude to about 30 feet

- Pick appropriate colors for all of the features

- Fly through campus and have fun

Turn in:

- An aerial view of campus from the Frank building looking across campus

- An aerial view of campus from the college lake looking across campus

The above will get you a B grade.

Extra activities – do either of these for an A grade:

- Take the Guilford College aerial photo from the web page, georeference it, and drape it over the TIN above.  Send me a picture of it.

- Create an animated fly-through of the campus with at least 10 stops.  Show me your movie

Part 2:  The Earth

- Load the file globalelevsmall.tif into ArcScene.

- Use this same file as the base height elevation information

- Change the vertical exaggeration to something reasonable (under View(Scene Properties)

- Change the color display of the image to something prettier

- This image is 1638 pixels wide, which we know corresponds to about 40,000 km.  The height of the Himalayas is about 8km.  Set the vertical exaggeration to a value that gets this about right.  What value is this? ___________

Turn in:

- An image showing the whole map

- An image showing the Himalayas at the appropriate scale