<!DOCTYPE HTML PUBLIC "-//W3C//DTD HTML 4.0 Transitional//EN"><!-- saved from url=(0056)http://resolute.gerg.tamu.edu/~woody/gmt/grdcontour.html -->NAME

grdcontour - contouring of 2-D gridded data sets

SYNOPSIS

grdcontour   grdfile   -Ccont_int   -Jparameters

[-Aanot_int[ffont_size][aangle][/r/g/b][o]] ] [ -Btickinfo ]

[-Ddumpfile ] [ -Eazimuth/elevation ] [ -Fred/green/blue ]

[-Ggap/width ] [ -K ] [ -Llow/high ] [ -M[flag] ] [ -N[unit]]

[-O ] [-P ] [ -Qcut ] [ -Rwest/east/south/north[r] ]

[-Ssmoothfactor   ]   [-T[+|-][gap/length][:LH]   ]

[-U[/dx/dy/][label] ] [ -V  ] [ -Wtype[pen] ] [ -Xx-shift ]

[-Yy-shift ] [ -Zfactor[/shift] ] [ -ccopies ]

DESCRIPTION

grdcontour reads a 2-D gridded file and produces  a  contour

map by tracing each contour through the grid.  As an option,

the x/y/z positions of the contour lines may be dumped to  a

single multisegment file or many separate files.  PostScript

code is generated and  sent  to  standard  output.   Various

options that affect the plotting are available.

No space between the option  flag  and  the  associated

arguments.   Use  upper  case for the option flags and lower

case for modifiers.

grdfile

2-D gridded data set to be contoured

-C    The contours to be drawn may be specified  in  one  of

three possible ways:

If cont_int has the suffix ".cpt" and can be opened  as

a file, it is assumed to be a color palette table.  The

color boundaries are then used as contour  levels.   If

the  cpt-file  has  anotation  flags in the last column

then those contours will be anotated.   By  default  no

contours are labeled; use -A to anotate all contours.

If cont_int is  a  file  but  not  a  cpt-file,  it  is

expected  to  contain  contour levels in column 1 and a

C(ontour) OR A(nnotate) in col 2. The levels  marked  C

(or  c)  are  contoured, the levels marked A (or a) are

contoured and annotated.  Optionally,  a  third  column

may  be  present  and contain the fixed anotation angle

for this contour level.

If no file is found, then cont_int is interpreted as  a

constant contour interval.  If -A is set and -C is not,

then the contour interval is set equal to the specified

anotation interval.

If a file is given and -T is set,  then  only  contours

marked with upper case C or A will have tickmarks.

-J    Selects the  map  projection.  Scale  is  inch/degree,

1:xxxxx. or width in inch (upper case modifier).

CYLINDRICAL PROJECTIONS:

-Jclon0/lat0/scale (Cassini)

-Jmscale (Mercator - Greenwich and Equator as origin)

-Jmlon0/lat0/scale (Mercator - Give meridian and  stan-

dard parallel)

-Joalon0/lat0/azimuth/scale (Oblique Mercator  -  point

and azimuth)

-Joblon0/lat0/lon1/lat1/scale (Oblique Mercator  -  two

points)

-Joclon0/lat0/lonp/latp/scale (Oblique Mercator - point

and pole)

- Jqlon0/scale  (Equidistant   Cylindrical   Projection

(Plate Carree))

-Jtlon0/scale (TM - Transverse Mercator)

-Juzone/scale (UTM - Universal Transverse Mercator)

-Jylon0/lats/scale (Basic Cylindrical Projection)

AZIMUTHAL PROJECTIONS:

-Jalon0/lat0/scale (Lambert).

-Jelon0/lat0/scale (Equidistant).

-Jglon0/lat0/scale (Orthographic).

-Jslon0/lat0/scale (General Stereographic)

CONIC PROJECTIONS:

-Jblon0/lat0/lat1/lat2/scale (Albers)

-Jllon0/lat0/lat1/lat2/scale (Lambert)

MISCELLANEOUS PROJECTIONS:

-Jhlon0/scale (Hammer)

-Jilon0/scale (Sinusoidal)

-Jklon0/scale (Eckert VI)

-Jnlon0/scale (Robinson)

-Jrlon0/scale (Winkel Tripel)

-Jwlon0/scale (Mollweide)

NON-GEOGRAPHICAL PROJECTIONS:

-Jpscale (Linear projection for polar (theta,r) coordi-

nates)

-Jxx-scale[l|ppow][/y-scale[l|ppow]] (Linear, log,  and

power scaling)

More details can be found in the psbasemap manpages.

OPTIONS

No space between the option flag and  the  associated  argu-

ments.

- A    anot_int  is  annotation  interval  in  data  units.

Ignored   if  contour  levels  are  given  in  a  file.

[Default is no annotations].  Several  options  can  be

set  to  modify  the  form  of  the annotation.  Append

ffont_size to change font size [9],  append  /r/g/b  to

change color of text fill box [PAGE_COLOR], append aan-

gle to fix annotation angle [Default follows  contour],

and  append  o  to  draw the outline of the surrounding

text box [Default is no outline].

-B    Sets map boundary tickmark  intervals.  See  psbasemap

for details.

-D    Dump  the  (x,y,z)  coordinates  of  each  contour  to

separate files, one for each contour segment. The files

will be named dumpfile_cont_segment[_i].xyz, where cont

is  the  contour value and segment is a running segment

number for each contour interval (for  closed  contours

we append _i.)  However, when -M is used in conjunction

with -D a single multisegment file is created instead.

-E    Sets the viewpoint's azimuth and  elevation  for  per-

spective view [180/90]

-F    Sets the color used for Frame and annotation. [Default

is black]

-G    gap is distance in inch between each annotation  along

the same contour.  width is number of points over which

to estimate the best fitting slope for  contour  labels

[Default is 4/10].

-K    More PostScript code will be appended  later  [Default

terminates the plot system].

-L    Limit range: Do not  draw  contours  for  data  values

below low or above high.

-M    When used in conjunction with -D a single multisegment

file  is created, and each contour section is preceeded

by a header record whose first column is flag  followed

by the contour level.

-N    Appends unit to all contour labels  (assuming  - A  is

set).   If  no name is specified, the unit given in the

grdfile will be used [Default is no unit].

-O    Selects Overlay plot mode [Default initializes  a  new

plot system].

- P    Selects  Portrait  plotting  mode  [GMT  Default  is

Landscape, see gmtdefaults to change this].

-Q    Do not draw contours with  less  than  cut  number  of

points [Draw all contours].

-R    west, east, south, and north  specify  the  Region  of

interest.  To specify boundaries in degrees and minutes

[and seconds], use the dd:mm[:ss] format.  Append r  if

lower  left  and  upper right map coordinates are given

instead of wesn.  [Default is region defined in the grd

file].

-S    Used to resample the contour lines  at  roughly  every

(gridbox_size/smoothfactor) interval.

-T    Will draw tickmarks pointing in the downward direction

every  gap along the innermost closed contours.  Append

gap and tickmark  length  (in  inch)  or  use  defaults

[0.2/0.04].   User  may choose to tick only local highs

or local lows by specifying -T+ or - T-,  respectively.

Appending  :LH  will plot the characters L and H at the

center of closed innermost  contours  (local  lows  and

highs).  L and H can be any single character (e.g., LH,

-+, etc.)  If a file is given by -C and -T is set, then

only  contours  marked with upper case C or A will have

tickmarks [and anotation].

-U    Draw Unix System time stamp on plot.  User may specify

where the lower left corner of the stamp should fall on

the page relative to lower left corner of plot in  inch

[Default   is  (-0.75,-0.75)].   Optionally,  append  a

label, or c (which will plot the command string.)

-V    Selects verbose mode, which will send progress reports

to stderr [Default runs "silently"].

-W    type, if present, can be 'a' for annotated contours or

'c'  for  regular  contours  [Default].   pen  sets the

attributes for the particular line.  Default values for

annotated  contours:  width = 3, color = black, texture

= solid.  Regular contours have default width = 1.

-X -Y

Shift  origin  of  plot   by   (x-shift,y-shift)   inch

[Default is (1,1) for new plots, (0,0) for overlays].

-Z    Use to multiply data values by factor [and  optionally

add  shift] before contouring starts.  (Numbers in A, -

C, -L refer to values after this scaling has occurred.)

-c    Specifies the number of plot copies. [Default is 1]

EXAMPLES

To contour the file  hawaii_grav.grd  every  25  mGal  on  a

Mercator  map  at  0.5  inch/degree,  annotate every 50 mGal

(using fontsize = 10), using 1 degree tickmarks, and draw 30

minute gridlines, try

grdcontour hawaii_grav.grd -Jm0.5 -C25 - A50f10  - B1g30m  >

hawaii_grav.ps

To contour the file image.grd using the levels in  the  file

cont.d  on  a  linear  projection  at 0.1 inch/x-unit and 50

inch/y-unit, using 20 (x) and 0.1 (y) tickmarks, smooth  the

contours  a bit, use "RMS Misfit" as plot-title, use a thick

red pen for annotated contours, and a thin, dashed, blue pen

for the rest, try

grdcontour image.grd -Jx0.1/50.0 -Ccont.d -S4 -B20/0.1:."RMS

Misfit":  -Wa5/255/0/0 -Wc1/0/0/255ta | lpr

BUGS

The text-outline box has not been implemented  for  perspec-

tive  view  plots.  Anotations will plot correctly, but con-

tours will go right through the text.

The labeling of local highs and lows may  plot  outside  the

innermost  contour  since only the mean value of the contour

coordinates is used to position the label.

There are too many options.

SEE ALSO

gmt, psbasemap, grdimage, grdview, pscontour