<!DOCTYPE HTML PUBLIC "-//W3C//DTD HTML 4.0 Transitional//EN"><!-- saved from url=(0053)http://resolute.gerg.tamu.edu/~woody/gmt/surface.html -->NAME

surface - adjustable tension  continuous  curvature  surface

gridding algorithm

SYNOPSIS

surface    [    xyzfile     ]     -Goutputfile.grd

-Ix_inc[m|c][/y_inc[m|c]]   - Rwest/east/south/north[r]  [

-Aaspect_ratio ] [ -Cconvergence_limit ] [ -H ] [ -Lllower  ]

[   -Luupper   ]  [  -Nmax_iterations  ]  [  -Q  ]

[-Ssearch_radius[m] ] [ -Ttension_factor[ib] ] [ -V[l] ]

[-Zover-relaxation_factor ] [ -: ] [ -b[d] ]

DESCRIPTION

surface reads randomly-spaced (x,y,z) triples from  standard

input  [or xyzfile] and produces a binary grdfile of gridded

values z(x,y) by solving:

(1 - T) * L (L (z)) + T * L (z) = 0

where T is a tension factor between 0 and 1, and L indicates

the Laplacian operator.  T = 0 gives the "minimum curvature"

solution which is equivalent to SuperMISP and the ISM  pack-

ages.   Minimum  curvature  can cause undesired oscillations

and false local maxima or  minima  (See  Smith  and  Wessel,

1990),  and  you  may  wish  to  use T > 0 to suppress these

effects.  Experience suggests T ~ 0.25  usually  looks  good

for  potential  field data and T should be larger (T ~ 0.35)

for steep topography data.  T = 1 gives a  harmonic  surface

(no  maxima  or  minima  are possible except at control data

points).  It is recommended that the  user  pre-process  the

data with blockmean or blockmedian to avoid spatial aliasing

and eliminate redundant data.  You may impose  lower  and/or

upper  bounds  on the solution.  These may be entered in the

form of a fixed value, a grdfile with values, or  simply  be

the minimum/maximum input data values.

xyzfile

3 column ASCII file [or binary, see -b] holding (x,y,z)

data  values.   If  no  file is specified, surface will

read from standard input.

-G    Output file name.  Output is a binary 2-D .grd file.

-I    x_inc [and optionally  y_inc]  is  the  grid  spacing.

Append m to indicate minutes or c to indicate seconds.

-R    west, east, south, and north  specify  the  Region  of

interest.  To specify boundaries in degrees and minutes

[and seconds], use the dd:mm[:ss] format.  Append r  if

lower  left  and  upper right map coordinates are given

instead of wesn.

OPTIONS

-A    Aspect ratio.  If  desired,  grid  anisotropy  can  be

added to the equations.  Enter aspect_ratio, where dy =

dx  /  aspect_ratio  relates   the   grid   dimensions.

[Default = 1 assumes isotropic grid.]

-C    Convergence limit.  Iteration is assumed to have  con-

verged  when  the  maximum  absolute change in any grid

value is less than convergence_limit.  (Units  same  as

data  z  units).   [Default is scaled to 0.1 percent of

typical gradient in input data.]

-H    Input file(s) has Header record(s).  Number of  header

records  can  be  changed  by editing your .gmtdefaults

file.  If used, GMT default is 1  header  record.   Not

used with binary data.

-L    Impose limits on the output solution.  llower sets the

lower  bound.   lower can be the name of a grdfile with

lower bound values, a fixed value, d to set to  minimum

input  value, or u for unconstrained [Default].  uupper

sets the upper bound and can be the name of  a  grdfile

with  upper  bound  values,  a fixed value, d to set to

maximum input value, or u for unconstrained [Default].

-N    Number  of  iterations.   Iteration  will  cease  when

convergence_limit  is  reached or when number of itera-

tions reaches max_iterations. [Default is 250.]

-Q    Suggest grid dimensions which have a highly  composite

greatest  common  factor.  This  allows  surface to use

several intermediate steps in  the  solution,  yielding

faster  run  times  and  better results. The sizes sug-

gested by -Q can be achieved by altering -R and/or - I.

You  can  recover the -R and -I you want later by using

grdsample or grdcut on the output of surface.

-S    Search radius.  Enter search_radius in same  units  as

x,y  data;  append m to indicate minutes.  This is used

to initialize the grid before the first  iteration;  it

is  not worth the time unless the grid lattice is prime

and cannot have regional stages.  [Default = 0.0 and no

search is made.]

-T    Tension factor[s].  These must be  between  0  and  1.

Tension  may  be  used  in the interior solution (above

equation, where it  suppresses  spurious  oscillations)

and in the boundary conditions (where it tends to flat-

ten the solution approaching the  edges).   Using  zero

for  both values results in a minimum curvature surface

with free edges, i.e. a natural bicubic spline.  Use  -

Ttension_factori   to   set  interior  tension,  and  -

Ttension_factorb to set boundary tension.   If  you  do

not  append i or b, both will be set to the same value.

[Default = 0 for both  gives  minimum  curvature  solu-

tion.]

-V    Selects verbose mode, which will send progress reports

to  stderr  [Default runs "silently"].  -Vl will report

the convergence after each iteration;  -V  will  report

only after each regional grid is converged.

-Z    Over-relaxation factor.  This  parameter  is  used  to

accelerate  the  convergence;  it is a number between 1

and 2.  A value of 1 iterates  the  equations  exactly,

and  will  always  assure  stable  convergence.  Larger

values overestimate the incremental changes during con-

vergence,  and  will  reach a solution more rapidly but

may become unstable.  If you use a large value for this

factor,  it  is  a  good idea to monitor each iteration

with the -Vl option.  [Default = 1.4 converges  quickly

and is almost always stable.]

-   :    Toggles    between    (longitude,latitude)    and

(latitude,longitude)    input/output.     [Default   is

(longitude,latitude)]

-b    Selects binary input mode  [Default is ASCII].  Append

d to indicate double precision [Default is single].

EXAMPLES

To grid 5 by 5 minute gravity block  means  from  the  ASCII

data  in  hawaii_5x5.xyg,  using  a tension_factor = 0.25, a

convergence_limit = 0.1 milligal, writing the  result  to  a

file  called  hawaii_grd.grd, and monitoring each iteration,

try:

surface hawaii_5x5.xyg -R198/208/18/25 -I5m -Ghawaii_grd.grd

-T0.25 -C0.1 -VL

BUGS

surface will complain when more than one data point is found

for  any  node  and suggest that you run blockmean or block-

median first.  If you did run blockmean/median and still get

this  message  it usually means that your grid spacing is so

small that you need more decimals in the output format  used

by blockmean/median.  You may specify more decimal places by

editing the parameter D_FORMAT  in  your  .gmtdefaults  file

prior  to  running  blockmean/median, or choose binary input

and/or output using single or double precision storage.

SEE ALSO

blockmean, blockmedian, gmt, nearneighbor, triangulate